## Slide 1: Impact Assessment of Climate Change on Water-Related Disasters for Building Up an Adaptation Strategy
Yasuto TACHIKAWA
Hydrology and Water Resources Research Lab.
Dept. of Civil & Earth Resources Engineering, Kyoto University

## Slide 2: Sousei Program (2012-2017)
Imminent global climate change (AORI, U Tokyo)
Stabilization target setting (JAMSTEC)
Risk Information (MRI)
Impact assessments (DPRI, Kyoto U)
Natural Disaster
Water Resources
Ecosystem
Climate variability and change
Integrated prediction system
Long-term projection
Large-scale variations
Probabilistic climate projection
Producing a standard climate scenario
PI: Prof. Nakakita (DPRI,Kyoto U)

## Slide 3: Key issues in SOUSEI PROGRAM
Generating PDF of extreme values with higher accuracy (New GCM data generation)
  PPE/SST ensemble to estimate uncertainty
  Use of regional scale model (RCM) to reduce local biases
Proposing adaptation and mitigation philosophy (Impact assessment of Climate Change)
  Projection of probabilistic risk
  Estimation of worst class cases
  Impact assessment, adaptation and mitigation strategy

## Slide 4: Research items
Projection of extreme
  Use of latest high-resolution GCM
  Dynamic perturbation
Reduction of uncertainty
  Improvement of model
  Ensemble projection
  TC ensemble
  Statistical downscaling
  Bias correction
  etc
Climate Projection
GCM/RCM Modeler
Impact Assessment
Adaptation

## Slide 5: Outlook SOUSEI Program for 2017
GCM results
Making model
Projection considering uncertainty, variability and worst class
Impact assessment, mitigation and adaptation
IPCC AR6
2012
2017
2014
2016
GCM results
natural disasters, water resources and ecosystem
Frist Stage
Second Stage

## Slide 6: Developing GCM and RCM by MRI, JMA
20km AGCM run with CMIP5’s SST
Dynamical Down Scaling by 5km NHM
(Three models)
Dynamical Down Scaling by 2km NHRCM
Improvement of processes in2km NHRCM
Coupling of 20km A-GCM with Ocean model
Run by 20km AO-GCM
Frist Stage
Second Stage
Validation of output from A-GCM , NHRCM
60km AGCM ensemble runs with CMIP5’s SST
2012
2014
2017

## Slide 7: Large number of GCM ensembles by MRI, JMA
YS
AS
KF
2.6
4.5
6.0
8.5
Present climate
Cluster 1
Cluster 2
Cluster 3
Ensemble mean
Different SST settings
RCP Scenario
PPE
60km AGCM by MRI
60km AGCM by ME
20km AGCM by MRI
Different cumulus convection parameterization

## Slide 8: Flood and inundation simulation under a changing climate
Worst case scenario simulation on flood and inundation under a changing climate; and
Probabilistic evaluation of magnitude and frequency on flood and inundation under a changing climate.

## Slide 9: Worst case scenario simulation on flood and inundation

## Slide 10: Future severe typhoon in GCM projection
Maximum Wind Distribution
A possible maximum typhoon realization in GCM projection under global warming.
Result from the 20-km GCM climate simulation in a future warming climate
Notes: Heavy rainfall and high winds under typhoon conditions strongly depends on the track and intensity of typhoons.
Owing to the limited number of the actual severe typhoons, the assessment of the typhoon hazards with various tracks and intensities of typhoons is difficult.
Therefore, numerically generating severe cases by controlling typhoon tracks is a viable alternative in increasing the number of extreme cases.
Furthermore, quantitative estimates of typhoon hazards are important for impact assessment applications.

## Slide 11
hPa
How water-related disasters will change
if typhoon takes different tracks?
(Ishikawa et al. 2013)
Notes: 11

## Slide 12: Virtual shifting of typhoon’s initial position- for making a worst scenario -
Virtual Shifting of typhoons initial position by keeping potential vorticity same
(a vorgas method)
Dynamic downscale by RCM
Worst case impact assessment on
Land： extreme wind and rainfall
Ocean： storm surge and wave height
NHM-5km
AGCM20
Ishikawa et al (2009)
Notes: 平成21年度の春以降に進んだ部分（スライド2枚中2枚目）

## Slide 13
Isewan Typhoon (1959) track and central pressure per 6hrs
Best track（black line）;
reproduction（blue）; and
pseudo-global warming experiment (pink color).
Isewan Typhoon (1959) pseudo-global warming experiment

## Slide 14
Control run
pseudo-global warming experiment
Oku et al., 2013
Virtual Shifting of typhoon’s initial position for the historical typhoon case (Isewan Typhoon, 1959)

## Slide 15: Flood and inundation simulations under the largest-class typhoons
Various scenarios of the largest-class typhoons under a changing climate
Flood and inundation simulations
The worst case impact assessment

## Slide 16: Flood and inundation disasters
Rainfall data under a changing climate
Rainfall-Runoff Model
including natural processes and dam operation
Inundation Model for lower flooding areas
Sediment transport/Land slide
Economic assessment
Storm surge

## Slide 17: Rainfall-Runoff Model
rainfall
evapotranspiration
Water flow from each slope
seepage

## Slide 18
Distributed rainfall-runoff
model

## Slide 19
Flood simulation by the Isewan Typhoon

## Slide 20
Wide-area inundation simulation model
Tokyo
Tone River, Edo River, Arakawa River,
Tokyo Bay
Nagoya
Kiso River, Shonai River, Ise Bay
Osaka
Yodo River, Neyagawa River, Osaka Bay
Sea
See water level
Flood water level and discharge
Main river
Urban river
Rainfall
Dyke broken, overflow
overflow

## Slide 21
Osaka area
Water depth distributuion after 6 hours
Wide-area inundation simulation model

## Slide 22: Future water resources projection in the Southeast Asian Region

## Slide 23
Future climate projection data using General Circulation Model developed by MRI, Japan
Current climate
experiment: 1979-2004
Near future climate
experiment: 2015-2039
Future climate
experiment: 2075-2099

## Slide 24
Precipitation (mm/h)
Sea Level Pressure (hPa)
MRI GCM simulation
20km spatial resolution, hourly

## Slide 25
GCM rainfall projection for the end of 21st century
Provided by Dr. Oku at DPRI, Kyoto University
Precipitation (mm/hr)

## Slide 26: GCM Projection data for runoff simulation
Surface runoff
generation
Canopy layer
Transpiration from root zone (daily)
Precipitation (daily)
Precipitation (hourly)
Soil layer
Evaporation from soil layer (daily)
Snowmelt (daily)
Sub-surface runoff generation
Snow accumulation
infiltration

## Slide 27: Research Methodology
River flow routing model
for estimating river flow discharge
using the future climate data such as
rainfall, evaporation and so on.
Input data
20 km resolution future
climate simulation data,
MRI-AGCM3.2S made by Morological Research Institute, Japan.
Analyzing
the changes river flow discharge for the assessment of water resources, flood risks and drought risks.
Present climate experiment: 1979-2008
Near future experiment: 2015-2044
Future climate experiment: 2075-2104

## Slide 28
Elevation (m)
Topography Data
using USGS HydroSHEDS
(Hydrological data and maps based on SHuttle Elevation Derivatives at multiple scale)
http://hydrosheds.cr.usgs.gov/index.php

## Slide 29: River Flow Routing Model
Flow direction
Elevation

## Slide 30: Future Water Resources Simulation in Thailand
Supattana Wichakul and Yasuto Tachikawa

## Slide 31
  Analysis Structure
GCM Data
Observation Data
Flow Routing Model (1K-FRM)
Simulated Discharge
Reservoir Operation Model
Hydrologic Model
Based on Infiltration Variable Capacity concept
Inundation Model
Bias Correction
Frequency Analysis of future discharge
Final result for future assessment

## Slide 32
For each 20km grid, a conceptual model with variable infiltration capacity concept is applied.
Surface Runoff
Groundwater
Subsurface runoff
Total Runoff
  Runoff Model
rainfall
evapotranspiration

## Slide 33
  Routing Model
runoff
Slope and river routing at each grid
  Runoff Model
Notes: The quadratic function was applied to flooded area where cross-section of the river was accordingly changed with the over bank flow. The criterion to distinguish the type of the cross section is set by the number of upstream grids. When the number is larger than 35,000 (about 35,000 km2) the quadratic cross section is adopted for representing the inundated areas. The value of B is equal to 1.06C^0.69; where C is catchment area at the points. These two values were determined and used in the Japanese catchment (Tachikawa et al., 2011).
To reproduce the inundation phenomena of the flood 2011 in Thailand, we assumed the quadratic cross section shape. The cross section parameter a was set to 0.00012 to reproduce a flood discharge properly.
In this study, we used the values of n and B same as the original model, n = 0.03 m-1/3s and 11.0 m-1/3s for channel and slope flow, respectively. If H= 10 m T= 577.35 m T=2*(h/a)^(1/2)

## Slide 34
Inundation Model
(a)
(b)
(c)
(d)
(e)
(f)
(g)
River cross section modeling
Water movement depending
on river and inundation depth
Notes: According to the value of indicating the lateral flow direction, the lateral inflow can be either positive or negative. To calculate water height in the floodplain pond hp, we set datum at the river bed and identify a suitable elevation for floodplain pond Elevp.
According to the value of ∆ℎ indicating the lateral flow direction, the lateral inflow can be either positive or negative. To calculate water height in the floodplain pond hp, we set datum at the river bed and identify a suitable elevation for floodplain pond Elevp.

## Slide 35
Dam reservoir operation model
Sources of Photo : http://kromchol.rid.go.th
Bhumibol dam
Sirikit dam
The Bhumibol dam at the Ping River basin : the capacity 13,420 MCM.
The Sirikit dam at the Nan River basin : the capacity of 9,510 MCM.
Notes: -if then rule
- dam operation model was embedded into some particular grids of 1K-FRM where the dams locate. An algorithm to develop a general reservoir operating rules was a flexible function that can be adjusted for different dam features.
-1964 The Bhumibol (BB) dam spillway capacity 6,000 m3/s .
-Afterwards, in 1974 the Sirikit (SK) dam the spillway capacity 3,250 m3/s for the multi-purposes in the Nan River basin.

## Slide 36
Simulation of dam reservoir operation
Bhumibol Dam Condition
Jan-Apr : release to downstream 200 m3/s
May-Dec : 15% of natural inflow
Sirikit Dam Condition
Jan-Apr : release to downstream 250 m3/s
May-Dec : 30% of natural inflow

## Slide 37
Runoff Simulation from March 1 to December 31 in 2011
Discharge in m3/s
Wang
Ping
Yom
Nan
C.2
A spatial distribution of estimated discharge on Oct 14, 2011

## Slide 38
At C. 2 station NSE = 0.91, RMSE = 388 m3/s, and R2 = 0.94
The parameter for the 1K-FRM in the routing part was Manning’s roughness coefficient n = 0.03 m-1/3s and 0.7 m-1/3s for channel and slope flows, respectively
Discharge simulation results
Notes: -To examine the applicability of the proposed method developed and embedded in the 1K-FRM, simulation was performed using input data obtained from the SXAJ model with model parameters listed in Table 3.2-1.
-Excess rainfall was then routed by the 1K-FRM, including the effects of dam release and inundation. Final results best fitting observed and simulated hydrographs are shown
-When data on simulated inflow including the inundation effect and observed inflow is analyzed, Nash-Sutcliffe efficiency (NSE) was 0.60 and 0.68, coefficient of determination (R2) was 0.61 and 0.73, and root mean square error (RMSE) was 320 m3/s and 275 m3/s at the BB and SK dams

## Slide 39
Effect of the Bhumibol and Sirikit dam
on flood 2011
Comparison of simulated discharge between actual situation, and without the BB and SK dams at C.2 station.

## Slide 40
Observation Data
Flow Routing Model (1K-FRM)
Simulated Discharge
Reservoir Operation Model
Hydrologic Model
Based on Infiltration Variable Capacity concept
Inundation Model
GCM Data
Sources of Photo : http://celebrating200years.noaa.gov/breakthroughs/climate_model/modeling_schematic.html
Discharge simulation using GCM outputs
Notes: General circulation model (GCM)
is the effective tool available today for well understanding of the interaction of the atmosphere, ocean, land surface, and ice for understanding of a changing climate behavior in long term.

## Slide 41
The latest version is MRI-AGCM3.2s: 1920×960 of grid cells of about 20 km spatial resolutions (cut 20 x 48 of grid cell throughout the Chao Phraya River Basin).
Three climate experiments under the SRES A1B scenario.
1. Present climate experiment : SPA (1979-2008).
2. Near future climate experiment : SNA (2015-2044). 3. Future climate experiment : SFA (2075-2144).
Output
GCM outputs used for discharge simulation

## Slide 42
Variability and trends of GCM outputs
Annual rainfall and (b) evapotranspiration data at the C.2 station grid.
Change in river discharge
Comparison of observed and simulated discharge with GCM outputs at the C.2 station
Trends of both observed and simulated discharge are compatible to increase at the 1.8 % and 2.5 % level.
(-1.9%)
(-0.6%)
(-7.2%)
(+4.6%)
(+4.1%)
(+6.8%)
River flow simulation used for GCM outputs without bias corrections
Notes: The figure shows trends of both observed and simulated discharge are compatible to increase at the 0.18 and 0.25 % level. -SPA runoff 19.7% of rainfall
-SNA runoff 18.6% of rainfall
-SFA runoff 20.1% of rainfall

## Slide 43
    GCM Data : MRI-AGCM3.2S, Resolution 0.1875 degree, 1,120 Grids (Cols=28 Rows=40)
Reference truth data
1. APHODITE daily rainfall :
Resolution 0.25 degree, 770 grids (Cols=22 Rows=35) available for 1979-2007
2. Evapotranspiration :
A monthly mean reference crop evapotranspiration (ETo) calculated by the Royal Irrigation Department of Thailand (RID) using the FAO Penman-Monteith method with recorded climatology data for the 30 years from 1981 to 2010.
The data were collected from 26 observing stations.
Bias correction of GCM outputs,
precipitation and evapotranspiration
Notes: Asian Precipitation–Highly-Resolved Observational Data Integration Towards Evaluation of Water Resources
APHODITE = A daily gridded precipitation dataset covering a period of more than 57 years (1951-2007) recorded data was created by collecting precipitation data from a local organization in each country and analyzing rain gauge observation data across Asia.
-To remove bias from the GCM Evapotranspiration data, the long term observed data are needed for the reference truth data. Unfortunately, there is no direct observation of the evapotranspiration.

## Slide 44
Bias correction of daily precipitation
Quantile-Quantile method
The GCM precipitation is mapped onto the observation precipitation at respective NEP of GCM quantile to observation quantile. This relationship can be mathematically expressed by the inverse of the observation data CDF as follows.
))
Transformation of the raw GCM precipitation data in baseline period.
Notes: Quantile-quantile (Q-Q) bias correction method was proposed for removing intensity bias from the GCM precipitation based on the assumption that correction can be conferred from ranked historical simulation or observation data to equivalent ranks in future projection.
-We did not assume the shape of the theoretical. To remove the bias in the training period, CDFs of both raw GCM and observation precipitation were created accordingly.

## Slide 45
Bias Correction of Evapotranspiration
Averages of mean monthly evapotranspiration
Present climate experiment
Near future climate experiment
Future climate experiment
Histograms comparing mean monthly evapotranspiration
Irrigation area effect
Notes: One of the important factors leading the ETo higher than the GCM evapotranspiration in the dry season is an effect for irrigated water. Most of the irrigation areas of the CPRB are located at the center of the basin.

## Slide 46
River discharge assessment under a changing climate
Low flow section of the flow duration curves constructed based on daily discharge of a period-of-record of each climate experiment.
Mean monthly discharge at the C.2 station for the present, near future and future climate experiments.
Duration curve of mean daily flow and standard deviation.

## Slide 47
Frequency analysis of extreme events
Maximum Daily discharge corresponding to different return periods for present climate (SPA), near future Climate (SNA) and future climate (SFA) for each location.
Tr=50 yr
Tr=30 yr
Tr=12 yr
at C.2 Sta.
at N.67 Sta.
at P.17 Sta.
at Y.16 Sta.
C.2
N.67
P.17
Y.16
N

## Slide 48
  Findings
Changes in the projected river discharge at the C.2 station, Nakorn Sawan province can be concluded that
the mean annual discharge tends to increase in both near future and future projection periods;
2) during a dry season the tendency of low flow in the near future period leads to decrease; and
3) GEV was applied for flood frequency analysis which indicates that flooding frequency has increased, leading high flood risk in the future.
Flood in the basin will have more severity; especially in the near future (2015-2043) the magnitude of 80-year return period flood (5,034 m3/s) is greater than the devastating 2013 Thai flood (4,686 m3/s). Therefore, adaptation measures to protect damages of flood in the country are critical to accomplish.
Notes: These findings of our study are also compatible with previous studies of Hunukumbura and Tachikawa (2012), and Kure and Tebakari (2012); but it is contradictory with the study result of Champthong et al., (2013).

## Slide 49: Future water resources projection in the Indochina Peninsula
Duong Duc Toan and Yasuto Tachikawa

## Slide 50: Study Area
Red River basin
Mekong River basin
Chao Phraya
River basin
Salween
River basin
Irrawaddy River basin
91.0o E
5.0o N
109.5o E
34.0o N

## Slide 51: Study area, data and hydrological model
Topographic data:
_ Topographic information used in the study was generated from processing the scale-free global streamflow network dataset with a spatial resolution of 5 arc minutes.
GCMs data:
_ MRI-AGCM3.2S (20-km resolution)
_ MRI-AGCM3.2H (60-km resolution)
_ MIROC5 (140-km resolution)
Hydrological model:
_ Flow routing model with kinematic wave flow approximation, 1K-FRM

## Slide 52
River Flow Simulation

## Slide 53: Projection of river discharge
Methods:
River discharge in the Indochina peninsula region was projected by feeding 3-hourly runoff generation data from MRI-AGCM3.2S dataset into flow routing model 1K-FRM.
Future changes in river discharge in the region were examined by comparing simulated discharge in the near future climate experiment (2015-2044) and future climate experiment (2075-2104) with the one in the present climate experiment (1979-2008).

## Slide 54
Changes in annual mean discharge
Ratio of annual mean discharge in the near future climate (left)
and the future climate (right) to the one in the present climate

## Slide 55
Changes in mean of annual maximum daily discharge
Ratio of mean of annual maximum daily discharge in the near future climate (left)
and the future climate (right) to the one in the present climate

## Slide 56
Changes in mean of annual minimum daily discharge
Ratio of mean of annual minimum daily discharge in the near future climate (left)
and the future climate (right) to the one in the present climate

## Slide 57: Statistical analysis of river discharge changes
Methods:
The statistical significance of river discharge changes in the Indochina Peninsula region was assessed by comparing means of projected river discharge data in the near future climate and the future climate with those in the present climate.
The test for statistical significance of river discharge changes is chosen based on the distribution of projected river discharge data.
_ Shapiro-Wilk W test was applied for data normality test.
_ The parametric Welch correction t-test was applied for the river discharge data which have a normal distribution.
_ The non-parametric Mann-Whitney U test was performed to test for statistical significance of non-normal distribution river discharge data.

## Slide 58
Statistical significance of changes
in annual mean river discharge
Statistical significant differences between annual mean discharge in the near future climate and present climate (left), and in the future climate and present climate (right)

## Slide 59
Statistical significant differences between mean of annual maximum daily discharge in the near future climate and present climate (left), and in the future climate and present climate (right)
Statistical significance of changes in annual mean maximum daily discharge

## Slide 60
Statistical significant differences between mean of annual minimum daily discharge in the near future climate and present climate (left), and in the future climate and present climate (right)
Statistical significance of changes in annual mean minimum daily discharge

## Slide 61: Future changes and uncertainties in river discharge projected using different ensemble experiments
Methods:
Changes in river discharge projected using different ensemble experiments of the MRI-AGCM and MIROC5 were compared to assess the uncertainties in projections of future climate change.
Statistical significance of changes in river discharge was also compared and evaluated.

## Slide 62: Future changes and uncertainties in river discharge projected using different ensemble experiments
Dataset | Resolution | Cumulus Convection Scheme | Sea Surface Temperature |  | Run name
MRI-AGCM3.2S | 20km | Yoshimura | Present Climate | Observation | YS_20
 |  |  | Future Climate | CMIP MME | YS_CMIP_20
MRI-AGCM3.2H | 60km | Yoshimura | Present Climate | Observation | YS_60
 |  |  | Future Climate | CMIP MME | YS_CMIP_60
 |  | Kain-Fritsch | Present Climate | Observation | KF
 |  |  | Future Climate | CMIP MME | KF_CMIP
 |  |  |  | Cluster 1 | KF_C1
 |  |  |  | Cluster 2 | KF_C2
 |  |  |  | Cluster 3 | KF_C3
MIROC5 | 150km | Chikira | Present Climate | Observation | MIROC5_P
 |  |  | Future Climate | CMIP | MIROC5_F
* Observation: Observational data by Hadley Center of Met Office, United Kingdom * CMIP MME: Coupled Model Intercomparison Project Multi-Model Ensemble |  |  |  |  | 

## Slide 63: Future changes and uncertainties in river discharge projected using different ensemble experiments
Ratio of annual mean discharge in the future climate
to the one in the present climate
YS_CMIP_20
YS_CMIP_60
KF_CMIP
KF_C1
KF_C2
KF_C3
MIROC5

## Slide 64: Future changes and uncertainties in river discharge projected using different ensemble experiments
YS_CMIP_20
YS_CMIP_60
KF_CMIP
KF_C1
KF_C2
KF_C3
MIROC5
Ratio of mean of annual maximum daily discharge in the future climate to the one in the present climate

## Slide 65: Future changes and uncertainties in river discharge projected using different ensemble experiments
YS_CMIP_20
YS_CMIP_60
KF_CMIP
KF_C1
KF_C2
KF_C3
MIROC5
Ratio of annual minimum daily discharge in the future climate
to the one in the present climate

## Slide 66
Statistically significant differences between annual mean discharge in the future climate and in the present climate
YS_CMIP_20
YS_CMIP_60
KF_CMIP
KF_C1
KF_C2
KF_C3
MIROC5

## Slide 67
Statistically significant differences between mean of annual maximum daily discharge
in the future climate and in the present climate
YS_CMIP_20
YS_CMIP_60
KF_CMIP
KF_C1
KF_C2
KF_C3
MIROC5

## Slide 68
MRI_YS_CMIP_20
MRI_YS_CMIP_60
MRI_KF_CMIP
MRI_KF_C1
MRI_KF_C2
MRI_KF_C3
MIROC5
Statistically significant differences between mean of annual minimum daily discharge
in the future climate and in the present climate

## Slide 69
Findings
There are discrepancies on the ratio of river discharge change and area of statistically significant increase or decrease among simulations using different GCMs datasets.
A clear change of river discharge was detected and found statistically significant in the Irrawaddy River basin, especially the annual maximum daily discharge in the future climate.
In the central part of Vietnam, a decreasing trend of annual minimum daily discharge in the future climate was found statistically significant from simulations using MRI-AGCM3.2S and MRI-AGCM3.2H datasets. However, the simulation using MIROC5 dataset displayed an opposite trend. This opposition also occurs at the Chao Phraya River basin and middle part of the Mekong River basin.
For future further work, more GCMs’ data will be used to evaluate the uncertainty in climate projection and to investigate the factors contributed to the simulation biases of river discharge.

## Slide 70
Thank you for your attention