## Slide 1
FLOOD EVENTS AS MAN-MADE/ NATURAL DISASTERS & THE EFFECTS OF CLIMATE CHANGE ON RAW WATER SUPPLY FOR MWA, THAILAND
* S. Wongsa
King Mongkut’s University of Technology Thonburi, Thailand
ASEAN Academic Networking in Water Disaster Management and Climate Change

## Slide 2
1. Flood in 2011
2. Experiments & Simulations of Dike Breach
3. Flood in Mekong River
4. Effect of Climate Change on Raw Water Supply, MWA
(MWA: Metropolitan Waterworks Authority)
Content of Presentation
ASEAN Academic Networking in Water Disaster Management and Climate Change

## Slide 3
- Five key tropical stroms
- Rainfall > 35%
- Dams operation
- High tides and strom surge
1. Flood in 2011

## Slide 4
Flood Frequency in Chao Phraya River Basin
1942
1975
1983
1995
2002
2006
2010
8
33 years
12
7
4
4
1
2011

## Slide 5
Historical Flood Events
Rattanakosin Kingdom (Bangkok, 1782 to present)
Years | Flood Depths (m)
1785 | : 4.20
1831 | > 4.20
1917 | : 2.00
1942 | : 2.27
1995 | > 2.27

## Slide 6
Historical Flood Events (1942)
Bangkok Railway Station
Victory Monument
Parliament
Royal Palace

## Slide 7
Chao Phraya River Basin.
Ping
Wang
Yom
Nan
Chao Phraya
Chao Phraya River Basin
total drainage area is approximately 157,924 km2, covering about 35% of the nation's land.
C.2

## Slide 8
Average Monthly Rainfall and Daily Discharge (1973-2008)
Ping
Chao Phraya
Ave. rainfall = 1,122 – 1,511 mm/year
C.2
P.1

## Slide 9
Tropical storms affected Thailand 2011.
(RID, Thailand)
Thailand Flood 2011

## Slide 10
Comparison of cumulative rainfall between (a) average annual rainfall (1950-1997) and (b) 2011. (HAII, Thailand)
(a)
(b)
Rainfall in 2011 > Ave. 35%

## Slide 11
The flood hydrograph at station C.2, Nakhon Sawan province. (RID, Thailand)
Discharge m3/s
6000
5000
4000
3000
2000
1000
0
Time (April-March, water year)
Qpeak = 4,686 m3/s
Volume = 52,961 MCM
(Ave. = 23,140 MCM)

## Slide 12
Location of dikes broken at (a) Bang Chom Sri Regulator (Location no.6) and (b) Left bank of Chao Phraya river. (RID)
(a)
(b)

## Slide 13
Failures of barriers protection of industrial parks.

## Slide 14
Flood in Don Muang international airport.
direction

## Slide 15
Continuity eq.
Momentum eq.
where h = water depth; u, v = depth averaged velocity components; tb = bed shear stress; r = water density; H = stage height (H = h + zb); zb = bed elevation; n = eddy viscosity; t = time; and x, y = spatial coordinate components in the Cartesian system.
iRIC: Nays2DFlood (http://i-ric.org/en/)

## Slide 16
Case I
Flood in 2011
Results and Discussions

## Slide 17
Simulation condition:
Manning’s n = 0.03, Dx = Dy = 140 m, SRTM DEM
(a) DEM (b) Inflow Flood Hydrograph

## Slide 18
(c) Time: 17 October 2011 (d) Time: 23 October 2011
(a) Time: 3 October 2011 (b) Time: 9 October 2011
Satellite Simulated

## Slide 19
Comparison of time series of flood depth and propagation between simulated results (right) and GISTDA satellite data (left).
(e) Time: 29 October 2011 (f) Time: 8 November 2011
Satellite Simulated

## Slide 20
River
Floodplain
Comparison of flood depth between simulated results (right) and measured data (IMPAC-T).
Satellite Simulated IMPAC_T

## Slide 21
Case II
Industrial Park
Simulation condition:
Manning’s n = 0.03, Dx = Dy = 100 m, SRTM DEM

## Slide 22
1.Saharattanakhon
2.Rojana
3.Hitech
5.Bang Pa-in
4.Factory Land
6.Navanakhon
7.Bangkadi
5 Oct.
9 Oct.
14 Oct.
12 Oct.
16 Oct.
17 Oct.
20 Oct.
Industrial Park

## Slide 23
(b-1) (present scenarios) (b-2) bank protection scenarios
Comparison of flood depth between present scenarios (before flood) and with bank protection scenarios (after flood).
Time: 8 days:
Time: 8 days:
Saharattanakhon
Saharattanakhon
Rojana
Rojana

## Slide 24
Comparison of flood depth between present scenarios (before flood) and with bank protection scenarios (after flood).
(a-1) (present scenarios) (a-2) bank protection scenarios
Time: 14 days:
Time: 14 days:
Saharattanakhon
Rojana
Rojana
Saharattanakhon
Hitech
Hitech
Bang Pa-in
Bang Pa-in

## Slide 25
Case III
Flood Diversion Channel
Simulation condition:
Manning’s n = 0.03, Dx = Dy = 100 m, SRTM DEM

## Slide 26: Module A5
Items | Q (m3/s)
West Flood Diversion Channel | 1,200
Mae Klong | 1,910
East Flood Diversion Channel 1 | 300
East Flood Diversion Channel 2 | 300
Tha Chin | 250~300
Q = 1,200 m3/s
Q = 500 m3/s

## Slide 27
Flood Diversion Channel
Q = 500 m3/s
Present condition 2011
With Flood Diversion Channel
Flood Diversion channel Chainat-Pasak
Chao Phraya
Chao Phraya
Thachin
Reduced Flood Depth & Areas

## Slide 28
Case IV
Floods & Return Periods
Simulation condition:
Manning’s n = 0.03, Dx = Dy = 100 m, SRTM DEM

## Slide 29
Return Periods at station C.2
Ping
Wang
Yom
Nan
Chao Phraya
Pasak
Return Periods Flood Discharge (m3/s)
2 2,320
5 3,342
10 4,018
25 4,872
50 5,506
100 6,134
150 8,000
C.2
In 2011: Qpeak = 4,686 m3/s
Simulation: Qpeak = 8,000 m3/s (150 yrs.)

## Slide 30
Present
with Diversion channel
Flood areas: same
Flood Return Periods 150 years
Qpeak = 8,000 m3/s
Chao Phraya
Thachin
Flood depth: >1.5 times
&propagation (of 2011)

## Slide 31
2.Experiments & Simulations of Dike Breach

## Slide 32
7.0 m
5.2 m
1.5 m
1.7 m
0.5 m
Elevation 1.2 m
Elevation -1.5 m
Dike
Concrete
Regulator
Floodplain
Circulate
reservoir
Dike Breach Experiment Setup
Notes: การทดสอบงานวิจัยนี้ เป็นการศึกษาพฤติกรรมการวิบัติของคันดินโดยการไหลของน้ำเป็นแบบราบเรียบและมีความลึก และพื้นที่หน้าตัดสม่ำเสมอกันตลอด จึงได้มีการออกแบบแปลงทดสอบและบ่อพักน้ำดังในรูป ซึ่งน้ำที่ใช้จะถูกสูบจากบ่อพักน้ำแล้วนำเข้าสู่แปลงทดสอบ

## Slide 33
Discharge Q = 4.14 l/s
0.50 m.
0.95 m.
Step 1 (60 min)
Step 2 (120 min)
Step 3 (180 min)
Step 1 (60 min)
Step 2 (120 min)
Step 3 (180 min)
Experiment: Overflow Type
Discharge Q = 7.78 l/s
Notes: เมื่อน้ำไหลล้นสันคันดิน จะทำให้เกิดแรงเฉือนพัดพาบริเวณสันคันดิน และเกิดการกัดเซาะบริเวณสันคันดินด้านหลัง ทำให้ความรุนแรงของกระแสน้ำเพิ่มขึ้น เนื่องจากมีช่องทางการไหลของกระแสน้ำเพิ่ม ส่งผลให้เกิดช่องแตกบนสันคันดินด้านหลังและขยายใหญ่ขึ้น จนทำให้บริเวณลาดเอียงของคันดินเกิดการทรุดตัวลงเช่นกัน ซึ่งการทดสอบที่อัตราการไหลแตกต่างกัน

## Slide 34
0.44 m.
1.34 m.
1.14 m.
Step 1 (60 min)
Step 2 (120 min)
Step 3 (180 min)
Step 1 (60 min)
Step 2 (120 min)
Step 3 (180 min)
Experiment: Overflow Type
Discharge Q = 11.59 l/s
Discharge Q = 16.84 l/s

## Slide 35
0.36 m.
0.44m.
Step 1 (60 min)
Step 2 (120 min)
Step 3 (180 min)
Step 1 (60 min)
Step 2 (120 min)
Step 3 (180 min)
Experiment: Earthen - Concrete Structures Type
Discharge Q = 4.14 l/s
Discharge Q = 7.78 l/s
Notes: ลักษณะการวิบัติของคันดินบริเวณรอยต่อโครงสร้างคอนกรีต จะเห็นได้ว่า ช่วงแรกเกิดการไหลซึมของน้ำบริเวณรอยต่อระหว่างคันดินและโครงสร้างคอนกรีต ทำให้บริเวณดังกล่าวเกิดการทรุดตัวและสไลด์ตัวลงเล็กน้อย เมื่อน้ำไหลล้นคันดินในช่วงระยะเวลาที่ 120 นาทีของการทดสอบ ทำให้คันดินบริเวณดังกล่าวถูกกัดเซาะและเกิดช่องขาดแผ่ขยายใหญ่ขึ้น

## Slide 36
0.57 m.
0.76m.
Step 1 (60 min)
Step 2 (120 min)
Step 3 (180 min)
Step 1 (60 min)
Step 2 (120 min)
Step 3 (180 min)
Discharge Q = 11.59 l/s
Discharge Q = 16.84 l/s
Experiment: Earthen - Concrete Structures Type

## Slide 37
Bang Chom Sri Regulator
Notes: การแตกของคันดินเนื่องจากน้ำล้นตลิ่งเกิดจากการกัดเซาะที่พื้นที่ผิวของลาดคันดิน

## Slide 38
3)ไซฟ่อนคลองระบายใหญ่ชัยนาท-ป่าสัก2
2)ปตร.บางโฉมศรี
ก่อสร้างแล้วเสร็จ ปี 2503
”(12.60 ล้าน ลบ.ม./วัน)
”1)ไซฟ่อนบางโฉมศรี
คลองส่งน้ำชัยนาท-อยุธยา
แม่น้ำเจ้าพระยา
(คลองเชียงราก)
Bang Chom Sri Regulator
Notes: การแตกของคันดินเนื่องจากน้ำล้นตลิ่งเกิดจากการกัดเซาะที่พื้นที่ผิวของลาดคันดิน

## Slide 39
Grid size:
Dx=1.0 x Dy=1.0 m.
Simulations of Dike Breach:
Bang Chom Sri Regulator
FLOW
D/S
U/S
Notes: การแตกของคันดินเนื่องจากน้ำล้นตลิ่งเกิดจากการกัดเซาะที่พื้นที่ผิวของลาดคันดิน

## Slide 40
3,600 s.
Simulations Results
Dike Breach at Bang Chom Sri Regulator
Notes: การแตกของคันดินเนื่องจากน้ำล้นตลิ่งเกิดจากการกัดเซาะที่พื้นที่ผิวของลาดคันดิน

## Slide 41
500 s.
800 s.
Simulations Results
Dike Breach at Bang Chom Sri Regulator
Notes: การแตกของคันดินเนื่องจากน้ำล้นตลิ่งเกิดจากการกัดเซาะที่พื้นที่ผิวของลาดคันดิน

## Slide 42
Simulations Results
Dike Breach at Bang Chom Sri Regulator
Notes: การแตกของคันดินเนื่องจากน้ำล้นตลิ่งเกิดจากการกัดเซาะที่พื้นที่ผิวของลาดคันดิน

## Slide 43
Simulations Results
Dike Breach at Bang Chom Sri Regulator
Notes: การแตกของคันดินเนื่องจากน้ำล้นตลิ่งเกิดจากการกัดเซาะที่พื้นที่ผิวของลาดคันดิน

## Slide 44
3. Flood in Mekong River

## Slide 45
Study areas

## Slide 46
Simulation Condition
- Model: Nay2dFlood
- DEM: SRTM DEM resolution 90 x 90 m.
- Simulation Grid: 100 x 100 m.
- Manning’s Coefficient n = 0.03
- U/S condition: Q = 9,000, 22,000 m.3/s
- D/S condition: free flow

## Slide 47
Flood Hydrograph in 1966
Chiang Sean: Qmax = 22,000 -23,000m.3/s
Jinghong: Qmax = 12,00 - 13,000m.3/s
Chiang Sean:
- ระดับตลิ่ง 11.80 ม. Q = 20, 025ม.3/วินาที
- ระดับเตือนภัย 8.50 ม. Q = 10,861 ม.3/วินาที

## Slide 48
Simulation Results: Q = 9,000 m.3/s
back water effect effect areas
Reaung River approximtely 1.5-2.0 km.
Kok River 1.5-2.0km.

## Slide 49
Flood wave propagation from Jinghong Dam to Chiang Sean approximately 1.5-2.0 days
Simulation Results: Q = 9,000 m.3/s

## Slide 50
no flood inundation areas
Chiang Sean:
- ระดับตลิ่ง 11.80 ม. Q = 20, 025ม.3/วินาที
- ระดับเตือนภัย 8.50 ม. Q = 10,861 ม.3/วินาที
Simulation Results: Q = 9,000 m.3/s

## Slide 51
back water effect effect areas
effect
Reuag River approximately 8.0-10.0 km.
Inundation areas
Ing River
Simulation Results: Q = 22,000 m.3/s
KokRiver approximately 5.0-10.0 km.

## Slide 52
Inundation areas
depth 1.0-3.0 m.
Simulation Results: Q = 22,000 m.3/s

## Slide 53
Climate Change
Shoreline erosion
Flood damage
What ‘d we do??
Ice loss from glacier

## Slide 54
Chao Phraya River; from Chao Phraya Dam, Chainat province to the Gulf of Thailand
Study area
Chao Phraya Dam
Fort Chula

## Slide 55
Mae Klong Dam
Thachin River
ChaoPhraya River
Kanchanaburi
Gulf of Thailand
Samlae Intake Station
Banglen Intake Statton
Bangkhen Water Treatment Plant
Samsen Water Treatment Plant
Thonburi Water Treatment Plant
Mahaswas Water Treatment Plant
30 Km.
Bangsue Water Treatment Plant
10 Km.
Phase 2 : 71 Km.
Phase 1 : 35 Km.
MWA: Metropolitan Waterworks Authority
Service areas: 3,192 km2,
Populations: 10 million,
Capacity: 5.5 million m3/day
Established in 1905
Notes: 55

## Slide 56
Changes in the Climate System - Ocean
Change in global average upper ocean heat content
Global average sea level change
(source : http://www.climatechange2013.org/images/report/WG1AR5_SPM_FINAL.pdf)

## Slide 57
Chart: ระดับน้ำเฉลี่ยรายปี สถานี C.4
| 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
ระดับน้ำเฉลี่ยรายปี 1977-2011 สถานี C.4 | 0.4526 | 0.65132 | 0.49926 | 0.68156 | 0.44277 | 0.38427 | 0.57277 | 0.42025 | 0.48926 | 0.38173 | 0.34929 | 0.45074 | 0.36301 | 0.38392 | 0.39353 | 0.34051 | 0.38656 | 0.43199 | 0.47236 | 0.38462 | 0.20181 | 0.30005 | 0.51252 | 0.57973 | 0.55397 | 0.67523 | 0.50696 | 0.50284 | 0.46748 | 0.66449 | 0.56605 | 0.55393 | 0.51345 | 0.63458
Chart: ระดับน้ำเฉลี่ยรายปี สถานี C.12
| 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
ระดับน้ำเฉลี่ยรายปี 1977-2011 สถานี C.4 | 0.42167 | 0.4053 | 0.34973 | 0.42422 | 0.23625 | 0.17634 | 0.41466 | 0.61192 | 0.40219 | 0.42418 | 0.47244 | 0.54663 | 0.71827 | 0.6944 | 0.52425 | 0.74093 | 0.58926 | 0.77598 | 0.50145 | 0.45619 | 0.69214 | 0.49036 | 0.57545 | 0.43227 | 0.39521 | 0.49317 | 0.38537 | 0.42578 | 0.42142 | 0.42002 | 0.41779 | 0.43199 | 0.80008 | 0.77153 | 0.48819 | 0.48022 | 0.63175 | 0.65891 | 0.64249 | 0.76211 | 0.59214 | 0.56888 | 0.59411 | 0.79471 | 0.68882 | 0.74577 | 0.68088 | 0.83603 | 0.7833
Memorial Bridge
Samsen
Water Level (MSL.)
Water Level (MSL.)
Average water level change in Thailand

## Slide 58
Projected changes over the 21st century in the Ocean: global average sea level change, IPCC
(source: www.grida.no/climate/IPCC_tar/wg1/fig11-12.htm)
A1FI (+48 cm)
in the year of 2100
A1Fl An emphasis on fossil-fuels (Fossil Intensive)

## Slide 59
(Upstream Boundary: discharges, Q(t) (Downstream Boundary: sea water level, h(t)
Methodology: MIKE11
Schematic of Chao Phraya River and longitudinal Profile
Chao Phraya Dam
Fort Chula

## Slide 60
Sea level change: IPCC SRES Scenarios (A1FI)
Model calibration & validation
Module | calibration | validation
HD Module | Jan. - Dec. 2008 | Jan. - Dec. 2010
AD Module | Jan. - Jun. 2008 | Jan. - Jun. 2010

## Slide 61
Schematic of Chao Phraya River
Model Setup
C.3
Sing Buri
C.7A
Ang Thong

## Slide 62
Calibration HD Module (Jan. - Dec. 2008)
Time
Water Level (m. MSL.)
(a) at station C.3
R2=0.88, IA = 0.94
Manning’s coefficient n = 0.022
(b) at station C.7A
R2=0.91, IA = 0.97
2008

## Slide 63
Validation HD Module (Jan. - Dec. 2010)
Time
Water Level (m. MSL.)
(a) at station C.3
R2=0.94, IA = 0.97
(b) at station C.7A
R2=0.93, IA = 0.98
Manning’s coefficient n = 0.022
2010

## Slide 64
Time
Salinity (g/l)
(a) at Bang Sai
R2=0.91, IA = 0.72
(b) at Samlae
R2=0.71, IA = 0.78
(c) at Phra Pradaeng
R2=0.91, IA = 0.87
Global Dispersion Factor = 500-1,800 m2/s, Global Exponent = 0.1-0.8 and Kmix = 500-1,800 hr-1
Calibration AD Module (Jan. - Jun. 2008)
2008

## Slide 65
Time
Salinity (g/l)
(a) at Bang Sai
R2=0.86, IA = 0.75
(b) at Samlae
R2=0.90, IA = 0.71
(c) at Phra Pradaeng
R2=0.96, IA = 0.94
Validation AD Module (Jan. - Jun. 2010)
Global Dispersion Factor = 500-1,800 m2/s, Global Exponent = 0.1-0.8 and Kmix = 500-1,800 hr-1
2010

## Slide 66
Model Application
Sea level rise compared with base year of 2008
  Year sea level rise
2025 + 8 cm
2050 + 17 cm
2075 + 33 cm
2100 + 48 cm
A1Fl An emphasis on fossil-fuels (Fossil Intensive)
A1FI (+48 cm)
in the year of 2100

## Slide 67
Sea level rise and Salinity concentrations (MWA’s criteria 0.25 g/l)
Year | salinity 0.25 g/l |  | Max. salinity at Samlae
 | Name of location | Distance from Chao Phraya Dam (km.) | (g/l)
2008 | Ban Kok Chang, Bang Sai | 164.0 | 0.293
2025 | Bang Sai, Bang Sai | 163.0 | 0.296
2050 | Maitra, Bang Sai | 161.0 | 0.300
2075 | BanPaeng, Bang Pa-in | 144.0 | 0.370
2100 | Ban Po, Bang Pa-in | 142.0 | 0.375
Model Application
(MWA’s criteria 0.25 g/l)

## Slide 68
With constant salinity concentration 30 g/l at the Gulf of Thailand
Year | salinity 0.25 g/l |  | Max. salinity at Samlae
 | Name of location | Distance from Chao Phraya Dam (km.) | (g/l)
2008 | Sai Noi, Bang Ban | 115.0 | 0.751
2025 | Bang Chanee, Bang Ban | 114.0 | 0.759
2050 | Bang Chanee, Bang Ban | 113.0 | 0.770
2075 | Phong Pheng, Pa Mok | 108.0 | 0.969
2100 | Pa Mok, Pa Mok | 106.0 | 0.987
Model Application
(MWA’s criteria 0.25 g/l)

## Slide 69
Solution to the problem of salinity intrusion in Chao Phraya River.
(a) divert flow from Chao Phraya Dam
(Q = 30, 35, 40, 45, 50, 55, 60 m3/s)
(b) divert flow from Mae Klong River
(Q = 0, 5, 10, 15, 20, 25, 30 m3/s)
(c) divert flow from Pa Sak River
(Q = 0, 5, 10, 15, 20, 25, 30 m3/s)
b.) Mae Klong River
a) .Chao Phraya Dam
c.) Pa Sak River
Samlae

## Slide 70
a. divert flow from Chao Phraya Dam
Discharge, Q (m3/s) | Max. Salinity at Samlae (g/l)
30 | 1.637
35 | 1.449
40 | 1.282
45 | 1.130
50 | 0.994
55 | 0.874
60 | 0.768
Model Application
> Salinity 0.25 g/l

## Slide 71
b. divert flow from Mae Klong River
Discharge, Q (m3/s) | Max. Salinity at Samlae (g/l)
0 | 0.987
5 | 0.873
10 | 0.768
15 | 0.675
20 | 0.592
25 | 0.519
30 | 0.455
Model Application
> Salinity 0.25 g/l

## Slide 72
c. divert flow from Pa Sak River
Discharge, Q (m3/s) | Max. Salinity at Samlae (g/l)
0 | 1.005
5 | 0.888
10 | 0.787
15 | 0.693
20 | 0.612
25 | 0.544
30 | 0.485
Model Application
> Salinity 0.25 g/l

## Slide 73
Relationship between divert flow discharge at Chao Phraya Dam and salinity at Samlae Intake station
Salinity 0.25 g/l, Q = 76.55 m3/s
divert flow from Chao Phraya Dam
Discharge, Q(m3/s)
Salinity (g/l)

## Slide 74
Salinity 0.25 g/l, Q = 40.19 m3/s
divert flow from Mae Klong River
Relationship between divert flow discharge at Mae Klong River and salinity at Samlae Intake station
Discharge, Q(m3/s)
Salinity (g/l)

## Slide 75
Salinity 0.25 g/l, Q = 41.96 m3/s
Relationship between divert flow discharge at Pa Sak River and salinity at Samlae Intake station
divert flow from Pa Sak River
Discharge, Q(m3/s)
Salinity (g/l)

## Slide 76
Thank you
sanit.won@kmutt.ac.th สนิท วงษา

## Slide 77: Dredging 2 and 4 m

## Slide 78
Effect of dredging on salinity intrusion in Chao Phraya River
Dredging 4 m
Dredging 2 m
Present condition